## Slide 1
AI for Magnetic Confinement Fusion
A. Agnello for the Fusion Computing Lab
HAMLET-Physics, Aug.19th-21st 2024

## Slide 2
The STFC Hartree Centre
High-performance computing, data analytics and artificial intelligence research facility located at the Sci-Tech Daresbury research and innovation campus

## Slide 3
AI activities at the Hartree Centre

## Slide 4
How to design
the fusion power plant of the future?
Iterative cycle
design – build – improve
is unfeasible
Can we get a full in silico replica
of a nuclear fusion reactor?
The Fusion Computing Lab
A collaboration with digiLab and the UKAEA

## Slide 5: Fusion Computing Lab
4-year collaborative agreement, aiming to continue beyond 2027
Around 60 individuals (mostly researchers + operational support, communications, etc.),
Evenly split between STFC and UKAEA
Secondments of UKAEA researchers at Hartree
Aim: to explore and implement advanced computing methods in nuclear fusion research, and workflows towards the development of a reactor digital twin
Agreements also with academic institutions (incl Univ. Manchester and University College London), US National Labs (ESCAPE Project), and SMEs

## Slide 6
WS-1:
Digital Thread co-integration
bringing it all together to build a digital twin
WS-2:
Fast and Actionable Emulators
using AI to replace expensive simulations with accurate surrogate models,
and to optimize the simulations to be run
WS-3:
Plasma Real-Time Control
AI-powered algorithms
to keep the plasma confined and safeguard the surrounding structures
WS-4:
Platform Architecture Exploitation
high-performance computing SW and HW solutions
WS-5:
Uncertainty Quantification
guarantee safe operations and understand sensitivity to design changes
WS-0:
Project Coordination, Training, Communication
Five
“Work Streams”
Fusion Computing Lab

## Slide 7
Plasma shape control
How do we keep the plasma where we want it to be?
Divertor Detachment
How do we cool the exhausts so not to damage the tokamak?
Core Turbulence and Gyrokinetics
How much energy is transported inside the “burning” plasma?
Disruptions
Can we predict/avoid/mitigate plasma instabilities?
Scrape-off Layer
How much energy is transported away from the “burning” plasma?
AI for Magnetic Confinement Fusion

## Slide 8
Surrogate Modeling

## Slide 9
Plasma Shape Control
example MAST-U equilibrium
Real time magnetic control of 2D shape of plasma in the poloidal plane.
High frequency control of actuator coil currents magnetically coupled to the plasma.
Generally tackled using linear control techniques.
Hartree AI researchers:
Nicola Amorisco, Adriano Agnello, George Holt, Abbie Keats, Alasdair Ross, Aran Garrod
UKAEA Collaborators:
Stan Pamela, James Buchanan, Graham McArdle, Charlie Vincent,
Kamran Pentland, etc.

## Slide 10
(Ohmic) Plasma Shape Control
MAST-U equilibrium
X-point
Strike point
Inner & outer midplane points
The plasma is confined by currents in the coils and in the plasma itself.
The "solenoid sweep" and other drives are preprogrammed to keep the plasma current up, but they can also alter its shape.
Probes around the tokamak give us noisy and incomplete information on the plasma. Is it departing from what we designed? And, how do we bring it back where it should be?

## Slide 11
‘Classical’ Plasma Shape Control
Real-time reconstruction
Observed state
Desired control targets
Design sweep
Coil currents
Probe measurements
Shape matrix
with the Shape matrix pre-calculated along the desired scenario.

## Slide 12
AI-supported Plasma Shape Control
‘Classical control’
AI / ML supported control
Wall/Passive currents are neglected
Dynamic
Wall/Passive currents are NOT neglected
Reinforcement Learning
Current framework
Shape matrix
emulation
Agnello et al. (2024), Phys.Plasmas, doi:10.1063/5.0187822 Amorisco et al. (2023), ICDDPS-4 and IAEA-FEC23
- GS surrogate: shape target emulator
- Accurate Shape matrices at any point in the experiment
MAST-U equilibrium
X-point
Strike point
Inner & outer midplane points
- Ensemble averages

## Slide 13
FreeGSNKE: FreeGS Newton-Krylov Evolutive
Fully Python non-linear solver for the evolutive equilibrium problem. Extends Ben Dudson’s FreeGS.
Static GS solver:
  forward-solve of Grad-Shafranov eq.,
  Newton-Krylov method.
Linear dynamics:
  Automated normal mode decomposition of passive structure model
  Linear stability analysis, linear growth-rate of vertical instability
Non-linear dynamics:
  NK-based solver of fully non-linear problem
  Prescribed time evolving profiles, parameterized by o, evolving
nonlinear
linearized
MAST-U VDE
Amorisco et al. (2024), Phys.Plasmas,
doi:10.1063/5.0188467
FreeGSNKE-RL library for RL experiments and training.

## Slide 14
Divertor Detachment
Background
Tokamak plasma exhaust is extremely energetic
There are no materials that would withstand unmitigated deposition of the exhaust
Advanced divertor configurations are being designed and tested to reduce the energy load on exhaust components
Problems we are addressing
Scrape-off layer and divertor simulation is computationally expensive but can be massively sped up with machine learning
Current control policies are based on linear theory but can potentially be improved with nonlinear policy development
Led by Hartree Centre and UKAEA, contributions from Lawrence Livermore National Laboratory and University of York
Central solenoid
Plasma-facing walls
Control coils
Divertor region
Scrape-off layer
Quarter cross-section of the MAST-U tokamak
G. K. Holt, et al, ICDDPS-4 (2023) G. K. Holt, et al., IAEA-FEC (2023)
A. Keats, et al., ICDDPS-5 (2024) G. K. Holt, et al., under review (2024)
Hartree: George Holt, Abbie Keats Collaborators: Stan Pamela1, Mike Kryjak2, Ben Dudson3, Lorenzo Zanisi1
1UKAEA, 2Univ. York, 3LLNL

## Slide 15
Divertor Detachment
Data set creation
Automation → scaling → HPC exploitation
  Automation
  Simulation input generation
  Convergence testing
  Diagnostic cleanup
  Scaling
  Trade-off between efficiency and wall time is problem dependent
  HPC exploitation
  Search space initialisation
  Simulation batching
  Array jobs
Supercomputer with nodes
Pool of simulations,
array jobs
Array job
Array job
Top: UMAP target visualisation. Bottom-left: job placement diagram. Bottom-right: search space initialization schematic.
G. K. Holt, et al, ICDDPS-4 (2023) G. K. Holt, et al., IAEA-FEC (2023)
A. Keats, et al., ICDDPS-5 (2024) G. K. Holt, et al., under review (2024)

## Slide 16
Divertor Detachment
Neural network training, results and interpretability
  Rigorous hyperparameter optimisation
  Tree-structured Parzen estimator for trial selection
  Asynchronous hyperband scheduler for culling
  Automated experiments, run to convergence
  Model performance
  Time-to-solution reduced from ~1 day to ~1 ms
  SHAP analysis
  Shapley additive explanations for global and local model interpretability
Top-left: hyperparameter tuning experiment progress. Top-right: trained model calibration plot. Right: Local SHAP interpretations. Bottom: Global SHAP interpretations.
G. K. Holt, et al, ICDDPS-4 (2023) G. K. Holt, et al., IAEA-FEC (2023)
A. Keats, et al., ICDDPS-5 (2024) G. K. Holt, et al., under review (2024)

## Slide 17
Accelerating Gyrokinetic simulations
Model: | Difficulty: | Caveats:
Fluid | easy 🙂 | No info on f(x,v) 😞
(quasi)linear gyrokinetic | Hard, but doable 🤨 | Can miss important physics 😞
Nonlinear gyrokinetic | Very hard, expensive 😞 | Provides f(x,v) info 🙂 But: how do we sample the parameter space fast and efficiently? 🤨
Transport in a plasma is governed by the phase space distribution f(x,v) of particles
Focus on slab ITG turbulence.
(Candy & Waltz, GA 2003)

## Slide 18
Accelerating Gyrokinetic simulations
Closures for nonlinear slab ITG turbulence: higher-order velocity moments as simple functions of lower-order moments.
Simpler than full-geometry problem, but gives good insight.
It also shows some behaviour that was not caught in “paper and pen” linear-Landau closures.
Hartree: Adriano Agnello Collaborators: JT Parker1,2, James Buchanan1, William Hornsby1,
1,Irish Centre for HE Computing, 2UKAEA
https://github.com/JosephThomasParker/SpectroGK

## Slide 19
QuaLiKiz
Surrogate
Surrogate uncertainty
Simulation database
JET
JET experimental 15D historical data
Fixed design space
Quasi-linear simulations
Active Learning on JET
Zanisi et al. (2024)

## Slide 20
QuaLiKiz
Surrogate
Surrogate uncertainty
Simulation database
Two Deep Ensembles
(Lakshminarayanan et al. 2017)
Classification
  Critical gradient estimation
  Prevents sampling in stable region
Regression
  ITG turbulence flux estimation
Zanisi et al. 2024
Active Deep Ensembles for Plasma Turbulence

## Slide 21
Zanisi et al. (2024) Nuclear Fusion doi:10.1088/1741-4326/ad240d
Siddle et al. in prep.
10x less data
4x less data
Classifier performance
Regressor performance
(ion particle flux)
Number of training examples
R2
F1
ADEPT Results on JET
Number of training examples

## Slide 22
Castagna et al. (2024), doi:10.1063/5.0189945 Physics of Plasmas
Speedup ~10x and complexity NlogN vs N2 of BOUT++
Using Generative Adversarial Networks as deconvolution operator for Large Eddy Simulations
StyleGAN for SOL Turbulence

## Slide 23
Unsupervised Disruption prediction
Predict impending plasma disruptions based on plant diagnostics in MAST database
Unsupervised approach vs literature work based on manually labelled data
Uncertainty-aware prediction for robust inference and advance warnings for mitigation
Unsupervised pre-training based on 𝛽-Variational Auto-Encoders
Training tailored to ensure robustness to missing data
RNN baseline prediction and customised transformers underway
RNN
Hartree: N. Amorisco, Wonny Lee UKAEA: Stan Pamela

## Slide 24
AI for magnetic confinement fusion
Detachment control
Emulators of Hermes-3 & SD1D
Efficiency with active learning
Interpretability with SHAP
Reinforcement learning for control
Gyrokinetics
Nonlinear slab gyrokinetic simulations of ITG turbulence
Data-driven closures discovery
Efficiency with active learning
SOL Turbulence
StyleGAN as deconvolution operator for large eddy simulations
Integrated into BOUT++
Disruption prediction
Plasma shape control
Evolutive Grad-Shafranov solver
Shape matrix emulation
Reinforcement learning for control
GPU support with JAX
MAST 8203
--- Past plasma current
--- Future plasma current
--- Prediction with uncertainty
Unsupervised approach eliminates need for manual labeling
Stack of VAEs for pre-training
Uncertainty-aware prediction