## Slide 1
“Absolute Luminosity For ATLAS”
– From installation to first physics data
Sune Jakobsen
On behalf of the ATLAS ALFA community
January 2012

## Slide 2
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
“Absolute Luminosity For ATLAS” – From installation to first physics data
Sune Jakobsen
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering
Agenda
ALFA detector system
Triggering of ATLAS by ALFA
Beam based alignment (scraping)
Beta* = 90 m program - determination of total cross section
Upgrade of Overlap Detector triggering
2/18

## Slide 3
“Absolute Luminosity For ATLAS” – From installation to first physics data
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
The ALFA detector system
Sune Jakobsen
3/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 4
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Absolute Luminosity For ATLAS - ALFA
Sune Jakobsen
Beam pipe
Beam pipe
Approach the beam to few mm with Roman Pot
Only used in dedicated high beta* runs
“Absolute Luminosity For ATLAS” – From installation to first physics data
4/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 5
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
“Absolute Luminosity For ATLAS” – From installation to first physics data
Sune Jakobsen
ALFA detector
500 µm scintillating fibers
Aluminum coating
5/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 6
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
“Absolute Luminosity For ATLAS” – From installation to first physics data
Sune Jakobsen
ALFA detector
Main detector
Main detector plan
Staggering of plans
5/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 7
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
“Absolute Luminosity For ATLAS” – From installation to first physics data
Sune Jakobsen
ALFA detector
Main detector
Overlap detector
Overlap detector plan
Overlap detector principle
5/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 8
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
“Absolute Luminosity For ATLAS” – From installation to first physics data
Sune Jakobsen
ALFA detector
Main detector
Overlap detector
Fiber connector
MultiAnode PhotoMultiplier Tube (MAPMT)
64 individual channels
MAPMT channel
5/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 9
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
“Absolute Luminosity For ATLAS” – From installation to first physics data
Sune Jakobsen
ALFA detector
Main detector
Main trigger tiles
Overlap trigger tiles
Overlap detector
Fiber connector
Main trigger scintillator tile
Overlap trigger scintillator tiles
5/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 10
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
“Absolute Luminosity For ATLAS” – From installation to first physics data
Sune Jakobsen
ALFA detector
Main detector
Main trigger tiles
Overlap trigger tiles
Overlap detector
Fiber connector
Main trigger scintillator tile
Overlap trigger scintillator tiles
Trigger fiber connector
5/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 11
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
“Absolute Luminosity For ATLAS” – From installation to first physics data
Sune Jakobsen
ALFA Roman Pot
Separates the detector from the ultra high beam vacuum
Threads for ferrite
Roman Pot window
Room for overlap detectors + trigger
Wall in front of the main detector
Secondary vacuum inside (detector side) to keep window flat
Window thickness 200 µm
6/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 12
“Absolute Luminosity For ATLAS” – From installation to first physics data
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Triggering of ATLAS by ALFA
Sune Jakobsen
7/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 13
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Current logic for main triggers
Sune Jakobsen
“Absolute Luminosity For ATLAS” – From installation to first physics data
8/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 14
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
Current logic for main triggers
“Absolute Luminosity For ATLAS” – From installation to first physics data
8/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 15
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction1 B7L1U and A7L1U not (B7L1L or A7L1L or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction2 A7R1L and B7R1L not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1U or B7R1U)
Single_Diffraction3 B7L1L and A7L1L not (B7L1U or A7L1U or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction4 A7R1U and B7R1U not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1L or B7R1L)
or
or
Examples of Look-Up-Tables
“Absolute Luminosity For ATLAS” – From installation to first physics data
9/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 16
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction1 B7L1U and A7L1U not (B7L1L or A7L1L or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction2 A7R1L and B7R1L not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1U or B7R1U)
Single_Diffraction3 B7L1L and A7L1L not (B7L1U or A7L1U or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction4 A7R1U and B7R1U not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1L or B7R1L)
or
or
“Absolute Luminosity For ATLAS” – From installation to first physics data
9/18
Examples of Look-Up-Tables
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 17
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction1 B7L1U and A7L1U not (B7L1L or A7L1L or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction2 A7R1L and B7R1L not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1U or B7R1U)
Single_Diffraction3 B7L1L and A7L1L not (B7L1U or A7L1U or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction4 A7R1U and B7R1U not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1L or B7R1L)
“Absolute Luminosity For ATLAS” – From installation to first physics data
9/18
Examples of Look-Up-Tables
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 18
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction1 B7L1U and A7L1U not (B7L1L or A7L1L or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction2 A7R1L and B7R1L not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1U or B7R1U)
Single_Diffraction3 B7L1L and A7L1L not (B7L1U or A7L1U or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction4 A7R1U and B7R1U not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1L or B7R1L)
“Absolute Luminosity For ATLAS” – From installation to first physics data
9/18
Examples of Look-Up-Tables
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 19
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction1 B7L1U and A7L1U not (B7L1L or A7L1L or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction2 A7R1L and B7R1L not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1U or B7R1U)
Single_Diffraction3 B7L1L and A7L1L not (B7L1U or A7L1U or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction4 A7R1U and B7R1U not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1L or B7R1L)
“Absolute Luminosity For ATLAS” – From installation to first physics data
9/18
Examples of Look-Up-Tables
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 20
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Sune Jakobsen
IP
B7L1U
B7L1L
A7L1U
A7L1L
A7R1U
A7R1L
B7R1U
B7R1L
Beam pipe
Elastics15 (B7L1U or A7L1U) and (A7R1L or B7R1L)
Elastics18 (B7L1L or A7L1L) and (A7R1U or B7R1U)
Single_Diffraction1 B7L1U and A7L1U not (B7L1L or A7L1L or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction2 A7R1L and B7R1L not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1U or B7R1U)
Single_Diffraction3 B7L1L and A7L1L not (B7L1U or A7L1U or A7R1U or A7R1L or B7R1U or B7R1L)
Single_Diffraction4 A7R1U and B7R1U not (B7L1U or B7L1L or A7L1U or A7L1L or A7R1L or B7R1L)
“Absolute Luminosity For ATLAS” – From installation to first physics data
9/18
Examples of Look-Up-Tables
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 21
“Absolute Luminosity For ATLAS” – From installation to first physics data
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Beam based alignment (scraping)
Sune Jakobsen
10/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 22
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Beam based alignment (scraping)
Sune Jakobsen
Beam pipe
“Absolute Luminosity For ATLAS” – From installation to first physics data
11/18
Beam loss monitor
Primary collimator
ALFA Roman Pot
Goal: Find accurately the beam center relative to the Roman Pots.
Position primary collimators at a well-defined position around 4 sigma.
Move in very slowly Roman Pots until they touch the beam.
Stop by BLM signal (or very high trigger rate).
Halo
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 23
“Absolute Luminosity For ATLAS” – From installation to first physics data
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Beta* = 90 m program
- determination of total cross section
Sune Jakobsen
12/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 24
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Data taking at 90 m beta* optics
Sune Jakobsen
Goal:
Physics data to determine total cross section.
Position:
6.5 sigma
Statistic:
ALFA PEB (only ALFA data, All ALFA_Any triggers): 55.7 M events.
Full ATLAS: 7.6 M events.
Standalone run: 10 M triggers (Any ALFA trigger).
Result:
Statistic sufficiently high. First offline feedback looks very promising.
Track pattern before cuts
“Absolute Luminosity For ATLAS” – From installation to first physics data
Track pattern for only elastic candidates
13/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 25
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Data taking – Standalone Overlap Detector run
Sune Jakobsen
Goal:
Align upper and lower detectors with high precision.
Method:
Using track passing though dedicated part of upper and lower detector.
Statistic:
Lower rate than expected. Run was extended (after the combined run) to get sufficient statistics. Total about 5 M triggers, but only low fraction is useful.
Result:
The distance can be determined, but more statistics would have been good.
Station nearest the IP
Observation:
The second station benefits in statistic due to showers from the first station.
Station furthest from the IP
“Absolute Luminosity For ATLAS” – From installation to first physics data
14/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 26
“Absolute Luminosity For ATLAS” – From installation to first physics data
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Upgrade of Overlap Detector triggering
Sune Jakobsen
15/18
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 27
“Absolute Luminosity For ATLAS” – From installation to first physics data
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Current situation
Sune Jakobsen
16/18
The OD signals arrive to late to ATLAS to be used to trigger all of ATLAS => Can be used in ALFA standalone data taking only.
Fast coaxial cables was chosen over air-core cables due to price. 1 air-core cable is about 10000 CHF (and 16 additional would have been needed).
Air-core cable signal
(Speed: 91 % of c)
Fast coaxial cable
(type c-50-3-1. Speed: 83 % of c)
Fast coaxial cable
(type c-50-3-1. Speed: 83 % of c)
Hit
Hit
Hit
Time
The rate of OD tracks in the 90 m run was much lower than expected. About 50 % of time used just for OD data taking.
Signal arriving to ATLAS
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 28
“Absolute Luminosity For ATLAS” – From installation to first physics data
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Upgrade plan
Sune Jakobsen
17/18
Using only the already installed air-core cable also for all OD signals.
All signals arrive to ATLAS in time and it is possible to distinguish OD and MD signals.
Air-core cable signal
(Speed: 91 % of c)
Hit
Hit
Hit
Time
Signal arriving to ATLAS
Only requires firmware upgrade of the Front End electronics (trigger mezzanine).
Different signal duration: 50 ns for MD signals, 25 ns for OD signals.
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 29
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Outlook
ALFA trigger upgrades will double the data taking efficiency. Implementation is ongoing.
New front end electronic for trigger signals will improve trigger efficiency.
In 2012 even higher beta* optics (500-1000 m) will be used in dedicated runs.
This will lead to better determination of the total cross section and maybe a luminosity determination (if the Coulomb Interference region is reached).
Sune Jakobsen
Beyond 2012 the LHC energy will go up and even higher beta optics will be used for total cross section and luminosity determination.
“Absolute Luminosity For ATLAS” – From installation to first physics data
18/18
A new readout mode (charge readout) to determine light yield of all scintillation fiber (aging check) is being implemented.
Determination of total cross section from 2011s beta* = 90 m runs and luminosity from ATLAS.
ALFA Triggering Beam based alignment Determination of total cross section Upgrade of Overlap Detector triggering

## Slide 30
“Absolute Luminosity For ATLAS” – From installation to first physics data
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Backup
Sune Jakobsen
7/30
90 m run 191373 Overlap Detector triggering Commissioning OD Trigger menu L1 in 2012 Trigger menu L2 in 2012 Summery

## Slide 31
ALFA hardware trigger upgrade and high beta* optics trigger menu for 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Needed changes in transmitting end (tunnel)
Sune Jakobsen
10/30
New firmware for trigger mezzanine:
All MD signals should give a 50 ns NIM signal out on the air-core cable.
All OD signals should give a 25 ns NIM signal out on the air-core cable.
The delay between input and output (leading edge) must be the same for MD and OD.
If MD and OD signal at the same time it should be treated as a MD signal.
The delay due to logic of the trigger mezzanine must be reduced by 25 ns.
90 m run 191373 Overlap Detector triggering Commissioning OD Trigger menu L1 in 2012 Trigger menu L2 in 2012 Summery
LED
MD signal on air-core
LED
OD signal on air-core
Firmware update made and tested on prototype.

## Slide 32
ALFA hardware trigger upgrade and high beta* optics trigger menu for 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Verification of functionality
Sune Jakobsen
13/30
Signal arriving in USA15 after ~280 m of air-core cable.
Signal quality sufficient to be recognized as a NIM signal.
Lin. out signal after first coincidence unit. Output signal width 25 ns like the input signal in ATLAS.
Input signal of 50 ns (from generator in lab)
0.5 V
20 ns
Preset out after first coincidence unit in ATLAS.
0.5 V
10 ns
Output from coincidence unit 2
Output from coincidence unit 3
Original output for timing reference
Input signal of 25 ns (from generator in lab)
Output from coincidence unit 2
Output from coincidence unit 3
Original output for timing reference
10 ns
0.5 V
10 ns
0.5 V
90 m run 191373 Overlap Detector triggering Commissioning OD Trigger menu L1 in 2012 Trigger menu L2 in 2012 Summery

## Slide 33
ALFA hardware trigger upgrade and high beta* optics trigger menu for 2012
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Distinguishing MD and OD signal with standard NIM electronics
Sune Jakobsen
12/30
Additional delay due to logic is 46 ns. From Front End firmware upgrade + CTP delay change: -50 ns.
Same ATLAS latency as for the ALFA runs in 2011.
The input to ATLAS is a standard NIM signal.
90 m run 191373 Overlap Detector triggering Commissioning OD Trigger menu L1 in 2012 Trigger menu L2 in 2012 Summery

## Slide 34
2/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Reference
All equation numbers, reference and figures refer to the Master thesis: “Performance evaluation and optimization of the luminosity detector ALFA”. The thesis can be found here:
http://cdsweb.cern.ch/record/1277003
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion

## Slide 35
4/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Definition of luminosity
Reference: [28](section 25, page 261) and [29].
One probe particle + one bunch with N1 particles
(8.1)
Figure 8.1 (11.3 in [29])
“Luminosity”
Probability for process with cross section σ:
The cross section area of the beam is A.
One bunch with N1 particles + one bunch with N2 particles
Figure 8.2 (1 in [30])
The luminosity is here defined to:
(8.3)
f is the frequency of the beam.
(8.4)
Equation (8.1) now becomes:
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion

## Slide 36
4/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Definition of luminosity
Reference: [28](section 25, page 261) and [29].
One bunch with N1 particles + one bunch with N2 particles
Figure 8.2 (1 in [30])
The luminosity is here defined to:
(8.3)
f is the frequency of the beam.
(8.4)
Equation (8.1) now gives the rate:
Assume Gaussian beam profile:
(8.3)
Inset transverse emittance and amplitude function:
(8.5)
The luminosity for nb bunched (using equation (8.3) and (8.5):
(8.7)
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion

## Slide 37
5/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Motivation for precise luminosity determination
Reference: [31]
Predictions from theories: Likelihood of events
Determination in ATLAS (next slide): number of times the events occur
Normalization (Link between theories and measurements): Luminosity
Figure 9.1 (from [32]) =>
<= Figure 9.2 (19-47 in [31])
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion

## Slide 38
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion
7/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
The large Hadron Collider at CERN
Reference: [1], [2], [5], [6], [7], [8], [9] and [10]
<= Figure 7.1 (from[4])
Figure 7.2 (from[4]) =>
ATLAS

## Slide 39
8/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Reference: [11] and [12]
ATLAS
(A Toroidal LHC ApparatuS)
Figure 7.3 (from[4]) =>
MBTS
LUCID
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion

## Slide 40
9/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Reference: [19], [21], [22], [30], [31], [34], [35], [36], [37] and [38]
Luminosity determination in ATLAS
Luminosity determination from the rate:
(8.4)
MBTS (Minimum Bias Trigger Scintillator)
LUCID (LUminosity Cherenkov Integrating Detector)
Liquid Argon Calorimeter
Inner detectors
Etc
Luminosity determination from van der Meer scan:
Large absolute uncertainty ~20 %
(8.3)
Determine the beam size by moving scanning the beams over each other (determining the cross section area A)
Dominated by errors on the number of particles N ~5 %
Luminosity determination from well-known processes
Z boson production
Large error on absolute scale
Two-photon production of e+e- pairs
Large error on background events
Two-photon production of µ+µ- pairs
Large error on background events
(8.4)
Best result yet: 11 % uncertainty
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion

## Slide 41
10/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Reference: [39](section 2.1)
Luminosity determination in ATLAS
Luminosity determination from Coulomb scattering (small t):
(10.8)
<= Figure 10.4 (2.1 in [39])
Challenge: The region of interest corresponds to scattering angle of about 3.5 µrad for 7 TeV protons
The same method was used at the SPS, but with a scattering angle of 120 µrad. Result: 3 % uncertainty.
The method will be used with the ALFA detector system (next slide).
Aim: 3 % uncertainty
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion

## Slide 42
12/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Reference: [39](section 5.1) and [42]
ALFA (Absolute Luminosity For ATLAS)
Requirements for the detector (Section 12):
1. Spatial resolution (vertical and horizontal) about 30 µm
2. Negligible inactive edge zone (< 100 µm)
3. Uniform trigger and detection efficiency (~100 % trigger efficiency)
4. Precise relative positioning of the detectors (<10 µm)
5. Operational in vacuum (mbar range)
6. Immunity to RF pick-up from the proton beam
7. Capable to cope with different beam positions
8. Moderate radiation hardness (kGy range)
9. Easy and quick to install and remove
10. Readout speed fast enough to identify each bunch crossing uniquely
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion

## Slide 43
14/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Reference: [39](section 6) and [42]
ALFA electronic - PMF
Voltage divider
PhotoMultiplier Frontend (PMF)
Passive board
Active board
Figure 13.27 - 13.30
0
Figure 13.31 (3 in [58])
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion

## Slide 44
15/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Reference: [39](section 6.6)
ALFA electronic - Motherboard
Embedded Local Monitor Board
Input from the temperature sensors
CAN bus connectors
Trigger signal input (TTC) (optical link)
Data output (optical link)
Voltage input
Connector to the trigger mezzanine
Connectors for kapton cable with up to 5 PMF
Figure 13.33 =>
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion

## Slide 45
17/57
NIELS BOHR INSTITUTE
UNIVERSITY OF COPENHAGEN
Performance evaluation and optimization of the luminosity detector ALFA
Sune Jakobsen
Reference: [39](section 4) + [42] (Typo in thesis page 80).
ALFA mechanics
Lower Roman Pot
Beam pipe
Lower bellow
Bottom level arm
Lower compensation bellow
Upper compensation bellow
Upper motor
Springs
Top level arm
Upper bellow
Figure 13.41 =>
Luminosity ATLAS at LHC ALFA Standard readout “Crosstalk” investigation Full detector readout Overlap detectors Test beam Conclusion