## Slide 1: XAFS Spectroscopy
Katarina Norén

## Slide 2
X-ray Absorption Theory
The absorpion coefficient - 
Transmission of intensity through a material
Lambert Beers’s Law:

## Slide 3
X-ray Absorption Theory
XANES = X-ray Absorption Near-Edge Structure
EXAFS = Extended X-ray Absorption Fine Structure
Variation in X-ray absorption coefficient as function of energy related to structural or electronic properties of sample

## Slide 4
Early Developments of XAFS
First noted in literature by students of Manne Siegbahn in Lund: Wilhelm Stenstöm and Hugo Fricke 1918-1920
Lots of early experimental and theoretical work in first 60 years of the 20th century

## Slide 6
Modern History
1960s and later: XAFS is a routine X-ray technique
Applications in catalysis, materials research, biology/life science, environmental and geosciences and others
SciFinder Search:
2001-2012: EXAFS/XAFS ~9900/3400 Publications
1960-1975: EXAFS/XAFS = 18/0 Publications
2011: EXAFS/XAFS ~800/350 Publications

## Slide 7
An Element Specific Technique
Thin-film
Catalysis
Coordination chemistry
Nano-structures
Metalloproteins
Enzymes
Environmental science
Low concentrations of metals
(Hg, Pb, Cr3+/Cr6+)
Chemistry and physics
Biochemistry
XAFS is applicable to systems in liquid, solid, solution and gaseous phase

## Slide 8
An Element Specific Technique
Thin-film
Catalysis
Coordination chemistry
Nano-structures
Metalloproteins
Enzymes
Environmental science
Low concentrations of metals
(Hg, Pb, Cr3+/Cr6+)
Chemistry and physics
Biochemistry
XAFS is applicable to systems in liquid, solid, solution and gaseous phase

## Slide 9
Properties of Synchrotron Light
High brightness: synchrotron light is extremely intense and highly collimated
Wide energy spectrum: synchrotron light is emitted with energies ranging from infrared light to hard x-rays
Tunable: it is possible to obtain an intense beam of any selected wavelength
Polarised: the synchrotron emitts highly polarised radiation

## Slide 10: MAX IV – A Synchrotron Light Facility
Electron injector
Linear accelerator
Storage ring
Beamlines
Insertion device

## Slide 11
Why Beamlines?
The storage ring and the insertion devices, also called light sources (bending magnets, undulators and wigglers) form the heart of the synchrotron radiation facility. However, the light sources as themselves are pretty useless for experiments.
The properties of the source are practically always manipulated: most importantly, the optical properties
      Wavelength
      Portion of high-order light
      Coherence
  but also geometrical properties like the size of the light spot used for experiments.
All this manipulation is done using the so-called beam lines.

## Slide 12
Main Functions of a Beamline
The beam line's main tasks are:
Monochromatize the radiation, this means that we need an energy dispersive element before the experiment
Transport the source to the experiment’s sample region as effectively as possible using (mostly) mirrors
    Transport
    Focus
    Take out the heat load (as early as possible)
Connects the experiment to the UHV environment of the storage ring

## Slide 13
Location of a Beamline
The location of a beamline is dictated weather the experimental techniques requires high energies (Wiggler beamline), high brightness (undulator beamlines) or very low energies and modest flux (bending magnets)

## Slide 14
Insertion Devices

## Slide 15
XAFS at Beamline I811
Optical design

## Slide 16
K
L
XAFS at Beamline I811
Experiment station
Si (111) crystals:
K-edge: S K-edge to As K-edge
L-edge: Zr L-edge to Au L-edge
Si (311) crystals:
K-edge: Fe K-edge to Mo K-edge
L-edge: Lu L-edge to Am L-edge

## Slide 17
X-ray Absorption Theory
The absorption of an x-ray photon
Absorption
Fluorescence
Auger effect

## Slide 18
X-ray Absorption Theory
The absorption of an x-ray photon
Transmission of intensity through a material:
Absorption: (E) = log(I0/I)
Fluorescence: (E)  If/I0
Typical experiment:

## Slide 19
X-ray Absorption Theory
The absorption of an x-ray photon

## Slide 20
Scientific Results - XANES data

## Slide 21
1628 - 1961
The Vasa

## Slide 22
S-XANES

## Slide 23
Scientific Results- EXAFS data
A little bit of data analysis
Fe3+(aq)

## Slide 24
Scientific Results
A little bit more data analysis
F.T.
Fe3+(aq)

## Slide 25
Fe – O distance
Model: 1.949 Å
XAFS: 1.977 Å
Result: Fe – O distance

## Slide 26
Conclusions
Oxidaton state
Coordination chemistry
Structural information (distances, angles, types of atoms)
Low detection limits (ppm)
Simple and fast technique