## Slide 1: ALICE: Upgrades & Perspectives

## Slide 2
Physics Motivation
Core Upgrade
  High Rate Capabilities
  ITS Upgrade
  Physics Performance Examples
Possible Additions
  VHMPID, MFT, FoCal
Summary

## Slide 3
The ALICE Setup

## Slide 4: Physics Motivation
Thermalization of heavy quarks in QGP:
  Baryon/meson for charm :Λc /D (maybe also Λb /B?)
  Elliptic flow
  Thermal production of charm? (D to low pT )
Quark mass dependence of energy loss in QGP:
  RAA for D and B mesons:
    Beauty via displaced D0  
    Beauty via displaced J/  ee
Exotic nuclear physics (hyper- and anti-nuclei)
Low-x structure and saturation (CGC?)

## Slide 5: Nuclear Modification
Quantified by:
Cronin Enhancement
Shadowing/Saturation
Jet-quenching
- yield relative to that from
N+N collisions, scaled for
the nuclear geometry (Nbin)

## Slide 6: Require
Improved ”impact parameter” resolution (ID)
Higher rates (statistics)

## Slide 7: Current TPC:
Effective dead time of 280µs, rate ≤3.5kHz

## Slide 8
The ALICE Setup
TPC
5m

## Slide 9: TPC Upgrade
new readout chambers
replace MWPC with GEMs
no gating, small ion feedback
usage of existing pad-planes possible
    momentum resolution for constrained tracks not affected
continuous sampling at 10 MHz, ship data unsuppressed off detector
needs new electronics
extensive R&D program ongoing with lab tests
confirm low ion feedback
  goal: 0.25% at gain of 2000
gain stability?
9

## Slide 10: Also need:
  Upgrade of all readout electronics
    pipelined readout of major ALICE detectors
  New, more performant, DAQ/HLT
    data compression requires on-line calibration and tracking
  common computing framework (DAQ/HLT/Offline)

## Slide 11: Event Size and Rates
  event size of major systems, I/O rates of online system
    assume average minbias rate to tape of 20 kHz
  data reduction for TPC: clustering, reconstruction
Detector | Event Size (MByte) After Zero After Data Suppression Compression |  | Input to Online System (GByte/s) | Compressed Output to data storage (GByte/s) Peak Average | 
ITS | 0.8 | 0.2 | 40 | 10.0 | 4.0
TPC | 20.0 | 1.0 | 1000 | 50.0 | 20.0
TRD (20 kHz) | 0.3 | 0.1 | 6 | 2.0 | 2.0
Others (1) | 0.5 | 0.25 | 25 | 12.5 | 5.0
Total | 21.6 | 1.55 | 1071 | 74.5 | 31.0
Data Format | Data Reduction Factor | Event Size (MB Pb-Pb) (MByte)
Raw data | 1 | 700
Zero suppression (FEE) | 35 | 20
Clustering (HLT) | 5-7 | ~3
Remove clusters not associated to relevant tracks (HLT) | 2 | ~1.5
Data format optimization (HLT) | 2-3 | < 1

## Slide 12: ITS Upgrade
factor 3 better secondary vertex resolution:
inner layer close to VTX(R = 2.2 cm)
smaller material budget
  thin sensors
  thinner beam pipe (ΔR = 800 µm)
fast readout
allow 50 kHz rate in Pb+Pb

## Slide 13
Upgrade Options
Two design options are being studied:
(Option A) 7 layers of pixel detectors
  better standalone tracking efficiency and pT resolution
  worse PID
(Option B)3 inner layers of pixel detectors and 4 outer layers of strip detectors
  worse standalone tracking efficiency and momentum resolution
  better PID
Radiation levels for layer 1:
  1 Mrad/1.6 x 1013 neqcm-2 per year
  with safety factor 4
6

## Slide 14
Improvement of Impact Parameter Resolution
Example: secondary vertex resolutions for D0  -+
D0  -+
7

## Slide 15
RAA and v2 of Prompt and Displaced D Mesons
Lint = 0.1 nb-1
Lint = 10 nb-1
Access to B meson via
B  D0 ( -+)
10

## Slide 16: Small-x Physics
enters new regime at LHC
  larger phase space than at RHIC
unique opportunity for ALICE
  use highest rapidity possible (η > 3), with significant pT range
  direct photon measurement cleanest!
    x-sensitivity, no final state effects
studies of gluon saturation
  expect transition from pQCD to CGC

## Slide 17: Nuclear Modification
Quantified by:
Cronin Enhancement
Shadowing/Saturation
Jet-quenching
- yield relative to that from
N+N collisions, scaled for
the nuclear geometry (Nbin)

## Slide 18: Saturation at RHIC and LHC
larger phase space for saturation effects at LHC
BRAHMS

## Slide 19
The ALICE Setup

## Slide 20: FoCal
SiW electromagnetic calorimeter
  two options for location
    3.5 m from IP, 2.5 < η < 4.2
    8 m from IP, 3.3 < η < 5.0
    optional hadronic calorimeter
2 technologies
  low-granularity conventional Si-pads
  high-granularity ≈ 1 mm2
    needed for π0/γ discrimination
    likely using MAPS
also allows studies of γ-jet correlations
4mm separation clearly detected
posters by T. Gunji (ID 498, 143),
N. Poljak (ID 118)

## Slide 21: ALICE Upgrade Physics Reach
Topic | Observable | Approved (1/nb delivered, 0.1/nb m.b.) | Upgrade (10/nb delivered, 10/nb m.b.)
Heavy flavour | D meson RAA | pT>1, 10% | pT>0, 0.3%
 | D from B RAA | pT>3, 30% | pT>2, 1%
 | D meson elliptic flow (for v2=0.2) | pT>1, 50% | pT>0, 2.5%
 | D from B elliptic flow (for v2=0.1) | not accessible | pT>2, 20%
 | Charm baryon/meson ratio (Lc/D) | not accessible | pT>2, 15%
 | Ds RAA | pT>4, 15% | pT>1, 1%
Charmonia | J/y RAA (forward y) | pT>0, 1% | pT>0, 0.3%
 | J/y RAA (central y) | pT>0, 5% | pT>0, 0.5%
 | J/y elliptic flow (forward y, for v2 =0.1) | pT>0, 15% | pT>0, 5%
 | y’ | pT>0, 30% | pT>0, 10%
Dielectrons | Temperature IMR | not accessible | 10% on T
 | Elliptic flow IMR (for v2=0.1) | not accessible | 10%
 | Low-mass vector spectral function | not accessible | pT>0.3, 20%
Heavy nuclei | hyper(anti)nuclei, H-dibaryon | 35% (4LH) | 3.5% (4LH)
pT coverage (pTmin) and statistical error for current ALICE with approved programme and upgraded ALICE with extended programme. Error in both cases at pTmin of “approved”.

## Slide 22: Possible running scenario
ALICE plans to run 6 years with upgraded detector, i.e. until 2026
(assuming start in 2019 and 2 years break of LS3)
Possible scenario:
  2019 – Pb–Pb 2.85 nb-1
  2020 – Pb–Pb 2.85 nb-1 (low magnetic field)
  2021 – pp reference run
  2022 – LS3
  2023 – LS3
  2024 – Pb–Pb 2.85 nb-1
  2025 – ½ Pb–Pb 1.42 nb-1 + ½ p–Pb 50 nb-1
  2026 – Pb–Pb 2.85 nb-1
This would not require pp running during high-luminosity runs, only a short time before a heavy-ion run for setting up and commissioning.

## Slide 23: Summary
  ALICE has strong physics program for precision QGP studies
    unique in rare low-pT probes
    requires ITS upgrade, enhanced rate capabilities + running beyond LS3
      significant R&D program for upgrades
  further enhancement of the ALICE setup under investigation, possibly
    strengthening muon measurement and high pT hadron ID
    exploring forward physics