## Slide 1: Status of the ADM-Aeolus wind lidar mission
A.G. Straume1, A. Elfving1, F. de Bruin1, A. Culoma1, T. Kanitz1, G. Labruyere1 , L. Mondin1, D. Wernham1, D. Schuettemeyer1, F. Buscaglione2, A. Dehn2, S. Casadio2, W. Lengert2
1ESA-ESTEC, The Netherlands, 2ESA-ESRIN, Italy
http://www.esa.int/esaLP/LPadmaeolus.html

## Slide 2: Aeolus teams
The Aeolus Mission Advisory Group
  Angela Benedetti / ECMWF
  Alain Dabas / MeteoFrance
  Pierre Flamant / IPSL
  Mary Forsythe / MetOffice
  Erland Källén / ECMWF
  Heiner Körnich / MISU
  Harald Schyberg / met.no
  Ad Stoffelen / KNMI
  Oliver Reitebuch / DLR
  Michael Vaughan / Lidar & Optics Associates
The Aeolus L1b, L2a and L2b algorithm development teams (DLR, ECMWF, IPSL, KNMI, MétéoFrance)
ESA Aeolus project and support teams (ESTEC, ESRIN, ESOC)
Airbus Defence and Space, and subcontractors

## Slide 3: Outline
ESA’s Earth Observation programme
Scientific motivation for ESA’s Doppler wind lidar mission
Instrument and measurement principle
Mission products and their envisaged use
Campaigns and CAL/VAL
Programmatic status
Conclusions

## Slide 4
ESA’s Earth Observation Programme
www.esa.int/livingplanet
BIOMASS
2020
Research driven
Earth Explorers
Core Missions
Opportunity Missions
GOCE
2009
EarthCARE
2016
ADM-Aeolus
2015
CryoSat 2
2010
SMOS
2009
Swarm
2013
ERS1
ERS2
Envisat
2 candidates
CarbonSat, FLEX
EE8
2022
?
Service driven
Earth Watch
MSG
MTG
Metop
Metop SG
Sentinel 1
Sentinel 2
Sentinel 3
Sentinel 4
Sentinel 5/5p
Meteosat
COPERNICUS
Operational Meteorology

## Slide 5: The importance of direct wind observations
ROSSBY RADIUS OF DEFORMATION
Global temperature soundings
Direct wind profile soundings (radiosondes)
g: gravitational acceleration, h: altitude, ω: angular
velocity of Earth’s rotation, φ: latitude (here 45°)
Aeolus sampling in 1 week
Direct wind observations are important at smaller scales

## Slide 6: Aeolus objectives
What are the scientific requirements?
Improve our understanding and predictability of
Atmospheric dynamics and global atmospheric transport
Global cycling of energy, water, aerosols, chemicals
How are they achieved?
Improved atmospheric analysis fields through use of Aeolus winds, in particular:
Tropics: Wind fields governs dynamics
Mid-latitudes: Intense storm developments and mesoscale circulation
What are the benefits?
  Better initial conditions for weather forecasting
  Improved parameterisation and modelling of atmospheric processes in climate and forecast models
Demonstrate the capabilities of space-based Doppler Wind LIDARs (DWLs) for global wind profiling and its potential for operational use

## Slide 7: Aeolus Mission
Doppler Wind Lidar
Direct Detection System
High Spectral Resolution
355 nm

## Slide 8: Aeolus measurement concept
(ALADIN)
80 mJ, 50 Hz
(= height)
Monostatic emit-receive path
(shown skewed)
Wind and atmospheric optical properties profile measurements are derived from the Doppler shifted signals that are back-scattered along the lidar line-of-sight (LOS)

## Slide 9: Measurement baseline
High Spectral Resolution: Separate molecular and a particle backscatter receivers
UV (355 nm , circularly polarized)
Cross-linear polarized light detected in polarizing scenes
Ground calibration (nadir and off-nadir)
Adjustable vertical sampling of atmospheric layers
  Δz: 0.25–2 km
  z: 0-30 km
Old measurement baseline
Example of ADM-Aeolus vertical sampling

## Slide 10: Measurement baseline
High Spectral Resolution: Separate molecular and a particle backscatter receivers
UV (355 nm , circularly polarized)
Cross-linear polarized light detected in polarizing scenes
Ground calibration (nadir and off-nadir)
Adjustable vertical sampling of atmospheric layers
  Δz: 0.25–2 km
  z: 0-30 km
Old measurement baseline
Example of ADM-Aeolus vertical sampling
New measurement baseline

## Slide 11: Aladin design

## Slide 12: Aeolus wind speed determination
Important to accurately determine the instrument responses to retrieve accurate wind speed.
  Dedicated calibration modes for this.
Use NWP T and p when retrieveing Dopplershift
Challenge to determine wind altitude representativeness within a layer in cases with strong wind shear
R: Rayleigh response
Frequency (pixel #)
Response

## Slide 13: Aeolus atmospheric products
Primary (L2b) product:
  Horizontally projected LOS (HLOS) wind profiles
    Approximately zonal at dawn/dusk (6 am/pm)
    3 km-averaged measurements and ~85 km observation averages – scene classified
    From surface to ~30 km in 24 vertical layers
    Random errors: 1-2(PBL), 2(Trop), 3-5(Strat) m/s
    Bias requirements: 0.5 m/s
Spin-off (L2a) products:
  Optical properties profiles
    , σ, OD, scattering ratio
    Cloud/aerosol cover/stratification
    Cloud/aerosol top heights
    Cloud/aerosol base height (optically thin)
    Aerosol typing (limited)
    3 km averaged measurements and <85 km observation averages – scene classified
Dusk/dawn orbit
Courtesy
N. Žagar
Flight direction
Powerful space-borne lidar with separate
molecular and particle backscatter detection
Near Real Time delivery of L1b data + L2b processor serves
* numerical weather prediction (NWP)
* potential for aerosol assimilation in
forecast and climate models

## Slide 14: Aeolus atmospheric products
Primary (L2b) product:
  Horizontally projected LOS (HLOS) wind profiles
    Approximately zonal at dawn/dusk (6 am/pm)
    3 km-averaged measurements and ~85 km observation averages – scene classified
    From surface to ~30 km in 24 vertical layers
    Random errors: 1-2(PBL), 2(Trop), 3-5(Strat) m/s
    Bias requirements: 0.5 m/s
Spin-off (L2a) products:
  Optical properties profiles
    , σ, OD, scattering ratio
    Cloud/aerosol cover/stratification
    Cloud/aerosol top heights
    Cloud/aerosol base height (optically thin)
    Aerosol typing (limited)
    3 km averaged measurements and <85 km observation averages – scene classified
Dusk/dawn orbit
Courtesy
N. Žagar
Flight direction
Powerful space-borne lidar with separate
molecular and particle backscatter detection
Near Real Time delivery of L1b data + L2b processor serves
* numerical weather prediction (NWP)
* potential for aerosol assimilation in
forecast and climate models

## Slide 15: L2A processor (P. Flamant, A. Dabas, V. Levert, P. Martinet)
Aims at reterieving the optical properties of the aerosols detected by the lidar: backscatter coefficient, extinction coefficient, backscatter to extinction ratio
ALADIN = first lidar in space able to discriminate particle from molecular backscatter
In principle, backscatter and extinction coefficients can be determined independently, there is no need for a priori values of the backscatter to extinction ratio
This opens the way to qualitative estimations of the type of aerosols, despite the lack of wavelength-dependent and polarization dependent information

## Slide 16: The lidar equation
Strength (in Watts) of a lidar signal as a function of the altitude z:
with
  K is a calibration constant.
  R(z) is the range from the lidar to the altitude z.
  b(z) is the backscatter coefficient (in m-1) of the atmosphere. It measures the capacity of the atmosphere to “reflect” the circularly polarized laser light.
  T2(z) (no unit, less than 1, decreasing function of range) is the transmission factor (measures photon loss ).
  a (in m-1) is the extinction coefficient of the atmosphere.
z
zsat
R(z)
The strength of the signal received by the lidar is a function of two optical, altitude dependant, parameters of the atmosphere, the backscatter b(z) and extinction coefficients a(z) of the atmosphere. Backscatter depend on scene polarization

## Slide 17: Aeolus - HSRL
For each observation, ADM provides to signals, one Rayleigh, one Mie, related to the optical parameters of the atmosphere via the equations:
where C1, C2, C3, C4, Kray and Kmie are characterized calibration constants.
In principle, it is possible to determine aaer(z) and baer(z) from the
equations above.
In practise, difficulties are encountered due to:
The lidar cannot distinguish absorption and scattering when detecting extinction
Large thickness of the height bin (vertical inhomogeneities give ambiguous results when solving the lidar equation)
Dependence on a priori T and p information
Only way to discriminate aerosol versus cloud particles: use β/α (non-trivial) or co-located cloud observations (not available at present)

## Slide 18: Variation of Aeolus sampling along the orbit
Extra-tropical scenario
Tropical scenario
Tropical scenario – no calibration
Co-location of Mie and Rayleigh channel sampling within an observation is essential
Terrain-
Following
model
Segment 1
Segment 2
Segment 3
Ellipsoid
Obs. 1
Obs. 3
Obs. 2
Obs. 6
Obs. 5
Obs. 4
Obs. 9
Obs. 8
Obs. 7
LUT
values
Courtesy G.J. Marseille

## Slide 19: Science related activities in support of the mission
Phase 0
  investigating data impact on NWP and atmospheric modelling
Phase A
  elaborating on system and data processing requirements (performance and end-to-end simulation tools), user requirements (impact studies), ground-based validation campaigns
  -> Lead to the scientific and technical mission concept which was evaluated and recommended at the Granada UCM in 1999
Phase B
  OSSE impact experiment, data assimilation, wind and cloud/aerosol statistics, signal processing, random and systematic errors and quality control
-> Leading to the 2001 Mission Requirements Document (MRD) and SRD
Phase C/D
  Wind and spin-off product processing, campaigns, product optimisation, further impact verification following baseline changes

## Slide 20: Mission Baseline changes resulting from hardware qualification
Change from Burst Mode (BM) to Continuous Mode (CM) operation in 2010 to ensure the necessary stable laser operation
Relaxation of the planned laser output power operation at the start of the mission from 110 to 80 mJ in 2012
ADM-Aeolus MAG:
  Is the mission still meeting the MRD, i.e. will the mission still provide beneficial atmospheric modelling and NWP impact?
  How to optimize the data processing?
Two parallel scientific Impact Study activities were launched to provide a consolidated answer using different tools and methods:
  KNMI, met.no, MISU/SMHI: Theoretical and Ensemble Data Assimilation impact experiment using simulated observations
  ECMWF: Impact of real observations adapted to the ADM-Aeolus sampling / properties in an Observing System Experiment (OSE)
Results will be shown in presentations
by M. Rennie and A. Stoffelen

## Slide 21: Aeolus campaigns
Objective:
  Validation of the predicted instrument radiometric and wind measurement performance using the Aladin Airborne Demonstrator (A2D)
  Establishing a dataset of atmospheric measurements obtained with an Aeolus type Lidar to improve algorithm development
2006 – 2009 A2D Campaigns:
  Two ground-based (2006, 2007) and three airborne (2007, 2008 and 2009)
  So far, on the order of 100 recommendations for the Aeolus mission (instrument and algorithm development and testing)
  First atmospheric measurements worldwide with a Fizeau and Double Fabry-Perot UV lidar system
A further pre-launch campaign in spring 2015 in order to:
  extend Rayleigh and Mie observations in highly heterogeneous conditions (vert./hor.)
  extend dataset on nadir response calibrations over ice and land
  rehearsal and preparation for CAL/VAL activities
Preliminary comparisons of A2D and DLR 2μm wind lidar measurements on-board the Falcon, near Greenland, 2009.
Courtesy: U. Marksteiner, DLR

## Slide 22: Aeolus CAL/VAL AO delta-call 2014
Aeolus CAL/VAL AO call, 2007:
Draft Phase E1 (and E) CAL/VAL plan and requirements established
Call open to experts/scientists worldwide
16 (joint) proposals received and reviewed
15 proposals were selected but now uncertain/no longer valid due to launch delays
DELTA AO CAL/VAL CALL NEEDED
Aeolus AO delta-call Objectives:
Allow for confirmation/update of current proposals
Attract new proposals
CAL/VAL Schedule:
Delta-call release: 1 May 2014, http://earth.esa.int/aos/AeolusCalVal
Phase E1 preparatory CAL/VAL Workshop end 2014 / early 2015:
  Refinement of CAL/VAL plan and compile implementation plan
  Campaigns planning and coordination amongst AO proposals and external campaigns
Launch (End 2015)
Phase E1 CAL/VAL Workshop/meeting (date TBC)
Phase E CAL/VAL monitoring and Workshops (coordinated by Mission Manager)

## Slide 23: Aeolus sampling and CAL/VAL requirements
Reference orbit: Equat. cros. time ascend node: 18:00 LT
Repeat cycle: 7 days
Track spacing in 1 week: ~300 km at mid lat
Example weekly coverage - one repeat cycle:
ADM-Aeolus: Scientific Cal. and Val. Requirements
  Detail Aeolus specifics concerning its wind and aerosol products and areas for special CAL/VAL attention:
  Available at http://earth.esa.int/aos/AeolusCalVal
T. Kanitz

## Slide 24: Why support our “BYO” CAL/VAL?
Early access to data (commissioning phase, first 3 months)
Access to data quality information, facilitating a good understanding of product quality and product use
Forum of exchange in learning how to work with the data from processing to visualization
Access to CAL/VAL data and results from other validation groups from ground-based to airborne and model assimilation experiments
Access to national funding sources and early preparation of your centre to assimilate Aeolus data

## Slide 25: Aeolus Project status
  The platform was completed in 2009, has been regularly health checked and delta-tested, and is being prepared for satellite integration early 2015
    In-situ Cleaning System is being implemented
    Satellite tests with VEGA to determine shock levels showed compliance
    Satellite characterization w.r.t. microvibrations by the reaction wheels: very low disturbance accelerations were measured at the laser position thanks to wheel dampers;
  The transmitter laser is the most challenging for the qualification
    The 1st flight laser transmitter operated for 5 weeks (August->September 2013) in vacuum: 150Mshots at 100-110 mJ output energy with ~7MHz frequency stability!
    Transmitter successfully passed full environmental qualification in autumn 2013
    Transmitter delivered to Airbus Defence & Space (Toulouse) for Aladin instrument integration and performance tests
    2nd and 3rd flight laser transmitters undergoing acceptance testing
  Aladin instrument delivery early 2015
  Flight Acceptance Review: November 2015

## Slide 26: Conclusions
The Aeolus wind lidar mission will deliver wind (suitable for data assimilation) and atmospheric optical properties products (could become suitable for NWP assimilation after R&D)
Aeolus L1b wind profiles (not corrected for temperature and pressure effects and no scene classification) will be delivered NRT together with a stand-alone processor
Impact studies has shown that recent measurement baseline updates will still allow for significant mission impact
CAL/VAL AO delta-call release: 1 May 2014, deadline 15 July
The Aeolus off-line L2a optical properties products will be made available to users off-line (now every 12 hours) but could in the future become available every 4 hours or more often
Aeolus laser qualification has recently been successfully completed, instrument integration and testing has started
Launch: End 2015

## Slide 27: An artist’s view of Aeolus in-flight
http://www.esa.int/esaLP/LPadmaeolus.html

## Slide 28: Spare slides

## Slide 29: Areas of concern to weather forecasting and climate modelling
Lack of homogeneous global coverage of direct wind profile measurements in the current Global Observing System (GOS)
Large uncertainties in the estimated contribution of aerosols and clouds to the global radiative forcing
Aeolus mainly addresses the first
and provides spin-off products in support of the latter
Radiosonde network

## Slide 30: Aeolus: ALADIN Laser Transmitter
The Master Oscillator is a stable resonator with an end-pumped rod. A crystal q-switch is used. Pulses of about 5 mJ energy at 1.06 um are generated.
Two diode pumped slab amplifiers generate about 350 mJ at 50 Hz pulse repetition frequency.
These IR pulses are frequency tripled to the UV (355 nm) in two harmonic generator crystals with ~35% efficiency.
UV optics to shape and steer the output beam for compatibility with ALADIN transmit optics.
laser transmitter in final integration

## Slide 31: AUX_CAL
Calibration coefficients defined by
where
  , , , , and are calibration constants,
  and are the molecular and particle backscatter,
  is the range from the satellite to the point at altitude z on the line-of-sight,
  and the molecular and particle transmission factors
N.B.: is the sum of the number of photons counted in channels A and B of the Rayleigh reciever (« useful » signals).

## Slide 32: AUX_CAL
If the calibration constant are known, the molecular and particle contributions to the signals can be separated:
From which it follows that
(Basis of the L2A processor)

## Slide 33: AUX_CAL
Coefficients to are computed from , and (transmission of the Fiseau determined from an ISR)
And and are estimated in a way similar to the generation of the AUX_CSR: useful signals of an IRC are predicted and compared to the real ones, and and are determined so that both match.

## Slide 34: Scientific Cal/Val Requirements
Understanding of the products and product properties
Consult product requirements (Mission Requirements Document)
Areas of special attention:
  Atmospheric sampling by the space-borne and validation instrumentation
    Horizontal (scene dependent)
    Vertical (scene and commanding dependent)
    Variable along the orbit
  Space-borne and validation product quality as function of
    measurement and retrieval technique
    atmospheric scene (clear and cloudy products, use of apriori)
  Complimentarity of different validation techniques
    Validation over different spatial and temporal scales
    Different information content
  Co-location criteria
  …

## Slide 35: L2A: Overarching view
L2A
Synthetic molecular signal
BRC Analysis
Group Analysis
L2A products
L1B data
Auxiliary data:
- meteorology,
- calibration,
- climatology.
In second step, identical features in the BRC scene are tentatively detected and processed independently.
First analysis at BRC level
Synthetic molecular signals = prediction of the Mie and Rayleigh signals the lidar should detect is there were no aerosols in the atmosphere (pure molecular signals). The signature of the aerosols is determined by comparing the signals actually detected by the lidar to these synthetic signals.

## Slide 36: L2A: Observation analysis
L1B data
BRC packing
ICA
SCA
Matching Bin Finder
Crosstalk correction
MCA
Auxiliary data:
- meteorology,
- calibration,
- climatology.
L2A products
Molecular data
MCA similar to Klett inversion. Requires the a priori knowledge of the BER.
SCA takes advantage of the presence of the two receivers. Needs Mie and Rayleigh bins are matching.

## Slide 37: L2A: Group analysis
L1B data
Feature Finder
SCA
Group packing
Crosstalk correction
Auxiliary data:
- meteorology,
- calibration.
L2A products
Molecular data
Scene Classification

## Slide 38: Feature Finder’s rationale
Based on the particle backscatter coefficient of the group
Horizontal Gaussian filter
Peak detection: group seeds
Parallel sprouting: aggregation of neighbour bins
  Criteria based on the group’s
4. Eviction of dubious groups (high relative error on )

## Slide 39: SCA on groups
2-bin periodic oscillations on
Need for averaging
Averaging with neighbours:
Creation of intermediate bins
1-bin-wide resolution kept in the sphere of influence of the averages

## Slide 40: Scene classification
Cloud-aerosol discrimination for each group, including averages centred on its upper and lower boundary:
A 16-classes flag:
  2 BERs :  0.05 sr-1 => Water cloud
  1 SR : > 2.5 => Water cloud
  NWP’s RH : > 94% => Water cloud
Consolidated by a 12-classes flag:
  NWP’s CLWC & CIWC : 4 domains (only vapour, liquid, mixed-phase, ice),
  NWP’s temperature , 2 boundaries 233.15 K and 273.15 K : 3 domains.

## Slide 41: L2A Conclusion
The L2A processor is now complete.
Fine tuning of settings still necessary, but the possible output products are there.
Full use of the possibilities offered by the High-Spectral-Resolution of the lidar requires matching Mie and Rayleigh bins ( constraint on the mission).
From now on, major refinements will come from real observations.