## Slide 1: Current status and plans of JMA operational wind product
Kazuki Shimoji
Meteorological Satellite Center
Japan Meteorological Agency

## Slide 2
Contents
Planning of JMA satellite systems
Statistics of MTSAT-1R/2 AMV
Plan for switching over from MTSAT to Himawari-8
Overview of Himawari-8 AMV
Summary

## Slide 3
Overview - Planning of JMA satellite systems (Himawari-series)
Satellite | Observation period
GMS | 1978 – 1981
GMS-2 | 1981 – 1984
GMS-3 | 1984 – 1989
GMS-4 | 1989 – 1995
GMS-5 | 1995 – 2003
GOES-9 | 2003 – 2005
MTSAT-1R | 2005 – 2010
MTSAT-2 | 2010 – 2015
Himawari-8 | 2015 – 2022
Himawari-9 | 2022 – 2029
GMS (Geostationary Meteorological Satellite)
MTSAT (Multi-functional Transport SATellite )
Back-up operation of
GMS-5 with GOES-9 by
NOAA/NESDIS
from May 22, 2003
to June 28, 2005
(GOES-9)
Aug 1981
GMS-2
(Himawari-2)
Aug 1984
GMS-3
(Himawari-3)
Sep 1989
GMS-4
(Himawari-4)
Mar 1995
GMS-5
(Himawari-5)
Feb 2005
MTSAT-1R
(Himawari-6)
Feb 2006
MTSAT-2
(Himawari-7)
Jul 1977
GMS
(Himawari)
Himawari
2014
Himawari-8
2016
Himawari-9
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸSS/L
ⒸMELCO

## Slide 4
Band | Central Wavelength [μｍ] | Spatial Resolution
1 | 0.43 - 0.48 | 1Km
2 | 0.50 - 0.52 | 1Km
3 | 0.63 - 0.66 | 0.5Km
4 | 0.85 - 0.87 | 1Km
5 | 1.60 - 1.62 | 2Km
6 | 2.25 - 2.27 | 2Km
7 | 3.74 - 3.96 | 2Km
8 | 6.06 - 6.43 | 2Km
9 | 6.89 - 7.01 | 2Km
10 | 7.26 - 7.43 | 2Km
11 | 8.44 - 8.76 | 2Km
12 | 9.54 - 9.72 | 2Km
13 | 10.3 - 10.6 | 2Km
14 | 11.1- 11.3 | 2Km
15 | 12.2 - 12.5 | 2Km
16 | 13.2 - 13.4 | 2Km
    Specification of Advanced Himawari Imager (AHI)
Band | Central Wavelength [μｍ] | Spatial Resolution
1 | 0.55 – 0.90 | 1Km
2 | 3.50 – 4.00 | 4Km
3 | 6.50- 7.00 | 4Km
4 | 10.3 – 11.3 | 4Km
5 | 11.5 – 12.5 | 4Km
MTSAT-1R/2
Full disk
(every 10 minutes)
rapidscan（every 2.5min）
RGB
HIMAWARI-8/9
Notes: This is a introduce of himawari-8 specification.
As you can see, number of bands will be increased from 5 to 16.
Spatial and time resolution will be 2 km and 10minutes.

## Slide 5
JMA plans to launch Himawari-8 in 2014 and begin its operation in 2015. Around early July, JMA will announce the launch date of Himawari-8.
The launch of Himawari-9 for in-orbit standby is scheduled in 2016.
Himawari-8/9 will be in operation at 140 degrees East covering the East Asia and Western Pacific regions for 15 years.
 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
MTSAT-1R Meteorological Mission MTSAT-2 Meteorological Mission |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Himawari-8 Himawari-9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
In-orbit standby
Operational
In-orbit standby
Manufacturing
Launch
In-orbit standby
In-orbit standby
Launch
Operational
Operational
Operational
In-orbit standby
Schedule for switching over from MTSAT to Himawari-8

## Slide 6
Contents
Planning of JMA satellite systems
Statistics of MTSAT-1R/2 AMV
Plan for switching over from MTSAT to Himawari-8
Overview of Himawari-8 AMV
Summary

## Slide 7
Production and Dissemination of MTSAT-operational AMV
IR1
WV
VIS
IR4
2015
2014
2013
RS
Standby
Standby
RS
Standby
RS
2012
Himawari-8
launched
Switchover
MTSAT-2 to
Himawari-8
Operational
MTSAT-1R
MTSAT-2
RS AMV is computed for internal use only

## Slide 8
Chart: BIAS and RMSVD of upper level IR AMVs (QI > 0.85) against radiosonde observation in the operation of MTSAT-1R and MTSAT-2
Historical statistic for Upper Level MTSAT AMV
O-B statistic for Jan. 2013
Negative wind speed BIAS was significantly improved by CCC and other method, but Negative BIAS still can be confirmed around jet in winter season
MTSAT-2
MTSAT-1R

## Slide 9
Historical statistic for Lower Level MTSAT AMV
Chart: BIAS and RMSVD of lower level IR AMVs (QI > 0.85) against radiosonde observation in the operation of MTSAT-1R and MTSAT-2
O-B statistic for Jan. 2013
Positive wind speed BIAS significantly debase quality of lower level AMV over tropical area
MTSAT-2
MTSAT-1R

## Slide 10
Historical statistic for WV MTSAT AMV (cloudy)
Chart: BIAS and RMSVD of WV AMVs (QI>0.85) against radiosonde observation in the operation of MTSAT-1R and MTSAT-2
positive wind speed BIAS in all season globally
negative wind speed BIAS around jet in winter season
O-B statistic for Jan. 2013
MTSAT-2
MTSAT-1R

## Slide 11
Contents
Planning of JMA satellite systems
Statistics of MTSAT-1R/2 AMV
Plan for switching over from MTSAT to Himawari-8
Overview of Himawari-8 AMV
Summary

## Slide 12
dissemination schedule for Himawari-8 AMV
Himawari-8 AMV
for evaluation
Operational MTSAT AMV
Operational Himawari-8 AMV
MTSAT AMV
for backup
April 2015
parallel dissemination
July 2015
Switchover to Himawari-8
launch
summer 2014
Test
Tuning
parallel dissemination via JMA FTP server
October 2015
operational AMV via GTS
Produced wind
VIS, IR and WV
Dissemination frequency
hourly
Data format
BUFR EDITION 4
Produced wind
VIS(0.64), WV(6.2,7.0,7.3) and 10.4
Dissemination frequency
hourly
Data format
BUFR EDITION 4
MTSAT
Himawari-8 ANV

## Slide 13
algorithm changes for Himawari-8 AMV
 | target selection | tracking | height assignment | quality control
MTSAT AMV | cloud analysis module for MTSAT AMV | cross-correlation method | IR-WV intercept and EBBT methods | EUMETSAT QI
Himawari-8 AMV | Himawari-8 cloud mask product based on NWCSAF and goes-R algorithm | Maximum Likelihood Estimation method using multiple cross-correlation surface | Maximum Likelihood Estimation | EUMETSAT QI
simultaneous utilization of information
wind vector and height are retrieved by maximizing likelihood function

## Slide 14
improvement to tracking accuracy
prior information
correlation surface from forward matching
auxiliary information
correlation surface from backward matching
posterior information
averaged correlation surfaces
set of
probable motion vectors
in forward matching
set of potential motion vector
set of
probable motion vectors
in backward matching

## Slide 15
optimal estimation for cloud height assignment
ground
To formulate forward model which gives a relationship between latent variable and observables
Conversion from the forward model to likelihood functions
maximizing sum of log likelihood functions

## Slide 16
Comparison of MTSAT and Himawari-8 algorithm
IR upper level AMV on Jan. 2013
MTSAT algorithm
H8 algorithm #1
H8 algorithm #2

## Slide 17
MTSAT algorithm
H8 algorithm #1
Comparison of MTSAT and Himawari-8 algorithm
IR lower level AMV on Jan. 2013
H8 algorithm #2

## Slide 18
MTSAT IR AMV computed by Himawari-8 AMV software (QI>80) for 00UTC 02 March 2014
Improvement to spatial coverage
operational
MTSAT IR AMV computed by operational software (QI>80) for 00UTC 02 March 2014
H8 AMV software

## Slide 19
MTSAT IR AMV computed by Himawari-8 AMV software (QI>80) for 00UTC 02 March 2014
MTSAT IR AMV computed by operational software (QI>80) for 00UTC 02 March 2014
operational
Improvement to spatial coverage over tropical region
H8 AMV software

## Slide 20
Summary
JMA will launch Himawari-8 around end of summer 2014.
operation of Himawari-8 (and relating products) will start from July 2015.
parallel dissemination of Himawari-8 AMV will start from April 2015 via JMA ftp server (as same as switchover from MTSAT-1R to MTSAT-2).
statistical quality and spatial coverage of Himawari-8 AMV will significantly change from that of MTSAT AMV.