## Slide 1: MOTION TRACKING AND CLOUD HEIGHT ASSIGNMENT METHODS FOR HIMAWARI-8 AMV
Kazuki Shimoji
Meteorological Satellite Center
Japan Meteorological Agency

## Slide 2
Contents
Introduction to Advanced Himawari Imager (AHI)
Tracking algorithm
Cloud height assignment algorithm
Result by new algorithm
Summary

## Slide 3
Band | Central Wavelength [μｍ] | Spatial Resolution
1 | 0.43 - 0.48 | 1Km
2 | 0.50 - 0.52 | 1Km
3 | 0.63 - 0.66 | 0.5Km
4 | 0.85 - 0.87 | 1Km
5 | 1.60 - 1.62 | 2Km
6 | 2.25 - 2.27 | 2Km
7 | 3.74 - 3.96 | 2Km
8 | 6.06 - 6.43 | 2Km
9 | 6.89 - 7.01 | 2Km
10 | 7.26 - 7.43 | 2Km
11 | 8.44 - 8.76 | 2Km
12 | 9.54 - 9.72 | 2Km
13 | 10.3 - 10.6 | 2Km
14 | 11.1- 11.3 | 2Km
15 | 12.2 - 12.5 | 2Km
16 | 13.2 - 13.4 | 2Km
    Specification of Advanced Himawari Imager (AHI)
Band | Central Wavelength [μｍ] | Spatial Resolution
1 | 0.55 – 0.90 | 1Km
2 | 3.50 – 4.00 | 4Km
3 | 6.50- 7.00 | 4Km
4 | 10.3 – 11.3 | 4Km
5 | 11.5 – 12.5 | 4Km
MTSAT-1R/2
Full disk
(every 10 minutes)
rapidscan（every 2.5min）
RGB
HIMAWARI-8/9
Notes: This is a introduce of himawari-8 specification.
As you can see, number of bands will be increased from 5 to 16.
Spatial and time resolution will be 2 km and 10minutes.

## Slide 4
motivation to innovate new tracking and height assignment method
Effective use of increased temporal and spatial information
= higher resolution AMV requested
= target box size should be minified for avoiding overlapping
= tracking accuracy debased due to lack of target feature information
Effective use of increased bands information
= improvement to CTH estimation
= simultaneous use of multiple bands needed
= JMA has no methods better than IR-WV intercept and EBBT for CTH estimation

## Slide 5
Contents
Introduction to Advanced Himawari Imager (AHI)
Tracking algorithm
Cloud height assignment algorithm
Result by new algorithm
Summary

## Slide 6
Image A (T = t0-1)
Image B (T = t0)
Image C (T = t0+1)
Target Area
Searching Backward
Searching forward
Cross-Correlation Tracking for MTSAT AMV
Correlation surface
of backward motion
Correlation surface
of forward motion
backward motion vector
used for consistency check
forward motion vector
final output vector

## Slide 7
correlation surface with small target box
(5x5 pixels)
Correlation Surface from small target box
many peaks = many similar patterns ->
Information included in target feature is not enough to determine wind vector accurately.

## Slide 8
set of
probable motion vectors
in forward matching
set of potential motion vector
motion vector estimation from forward matching
motion vector which maximize cross-correlation in forward matching is selected as an “best” forward motion vector
motion vector is determined only by forward matching information

## Slide 9
set of
probable motion vectors
in backward matching
set of potential motion vector
motion vector which maximize cross-correlation in backward matching is selected as an “best” backward motion vector
motion vector is determined by forward matching information only
motion vector estimation from backward matching

## Slide 10
Simultaneous use of matching information
set of
probable motion vectors
in forward matching
set of
probable motion vectors
in backward matching
set of potential motion vector
“best” vector in forward matching , but unlikely in backward matching
if difference between forward and backward motion vector is large, purged by temporal consistency check
= tracking failure

## Slide 11
Simultaneous use of matching information
Optimal motion vector should be selected from this intersection
temporally inconsistent vector should not be selected from the beginning
set of
probable motion vectors
in forward matching
set of
probable motion vectors
in backward matching
set of potential motion vector

## Slide 12
posterior information
averaged correlation surfaces
auxiliary information
Correlation surface from backward motion
prior information
Correlation surface from forward motion
probabilistic inference
to regard correlation surface as log likelihood function
Maximum Likelihood Estimation Approach for small Scale AMV
To equate cross-correlation with log likelihood function
To compute average of two log likelihood function surface from forward and backward matching
To search vector which maximize the averaged log likelihood function

## Slide 13
set of
possible backward motion vectors
how to find temporally consistent vector
prior information
correlation surface from forward matching
auxiliary information
correlation surface from backward matching
posterior information
averaged correlation surfaces
set of
probable motion vectors
in forward matching
set of potential motion vector
reversed for averaging

## Slide 14
prior information
correlation surface from forward matching
auxiliary information
correlation surface from backward matching
posterior information
averaged correlation surfaces
set of potential motion vector
Peak position on averaged surface corresponds to large CC points on both of FW and BW surfaces
how to search temporally consistent vector
reversed for averaging
set of
possible backward motion vectors
set of
probable motion vectors
in forward matching

## Slide 15
set of
possible small scale motion vectors
(similarity high)
set of
possible large scale motion vectors
(similarity high)
auxiliary information
correlation surface
from large target box
prior information
correlation surface
from small target box
posterior information
averaged correlation surfaces
set of potential motion vector
Application to spatially consistent vector

## Slide 16
forward motion small scale
forward motion large scale
backward motion
large scale
backward motion
small scale
Likelihood estimation
by temporal and spatial information
Notes: Information should be used separatelly

## Slide 17
forward motion small scale
forward motion large scale
backward motion
large scale
backward motion
small scale
Likelihood estimation
by temporal and spatial information

## Slide 18
sat:MTSAT-1R
Channel:IR10.8
time interval:5min
target size:5x5pix
tracking: normal
Green: natural
Red: noisy track
Target motion trajectories with small target box

## Slide 19
sat:MTSAT-1R
Channel:IR10.8
time interval:5min
target size:
5x5pix,15x15pix
tracking: time and space MLE
Green: natural
Red: noisy track
comparison to rapid scan tracking methods
by checking cloud trajectory

## Slide 20
Contents
Introduction to Advanced Himawari Imager (AHI)
Tracking algorithm
Cloud height assignment algorithm
Result by new algorithm
Summary

## Slide 21
IR channel radiance
NWP profile data
simultaneous use of radiance and motion vector
for cloud height estimation
EBBT method
Using single band radiance information
NWP profile is needed for conversion to pressure and considering atmospheric effects to observed radiance

## Slide 22
IR channel radiance
WV channel radiance
NWP profile data
simultaneous use of radiance and motion vector
for cloud height estimation
IR-WV intercept method
Using IR-WV bands radiance information
NWP profile is needed for conversion to pressure and considering atmospheric effects to observed radiance

## Slide 23
motion vectors
NWP profile data
simultaneous use of radiance and motion vector
for cloud height estimation
Best fit level method
Using motion vector information
NWP profile is needed for minimizing difference between AMV and NWP wind

## Slide 24
IR channel radiance
motion vectors
NWP profile data
simultaneous use of radiance and motion vector
for cloud height estimation
Maximum Likelihood Estimation
for cloud height assignment
Usable information for height assignment are radiance, motion vector and NWP profile data
Likelihood function to be maximized must be defined (no convenient information such as correlation surface)
Optimization algorithm required for searching optimal cloud height
WV channel radiance

## Slide 25
Forward model
ground
Radiance rationing of from high, middle, low and ground layer
10.5, 12.0 and 6.7 micro meter imagery are used
Averaged radiance in target box (5x5) is used

## Slide 26
ground
wind vectors derived from VIS, IR and WV imagery are available
Information of visible imagery is also available for height assignment by using VIS wind vector
usability of motion vectors for cloud height estimation
OR
OR

## Slide 27
Optimization Strategy
Not to minimize cost function but to maximize likelihood function which is set to 0-1 for handling not only “equation” but also “inequality” and fuzzy inference theory.
.NOT.
.GT.
.OR.
IF THEN
(1- )
Limit of cost function minimization (available for only simultaneous equation system)
.EQ.
.AND.
Likelihood function maximization
(available for simultaneous equation and inequality system and propositional logic)
In real computation, Cauchy distribution (and its CDF) used instead of normal distribution for searching optimal latent variables

## Slide 28
Optimization method - Differential Evolution method
Test function : Ackley's function
Too many local minima
⇒difficult to find optimal parameter by methods using derivative function
global minimum
Storn, R.; Price, K. (1997). "Differential evolution - a simple and efficient heuristic for global optimization over continuous spaces". Journal of Global Optimization 11: 341–359
initial points are changed by iteration of
mutation evolution
crossover
survival of the fit
operations .

## Slide 29
Contents
Introduction to Advanced Himawari Imager (AHI)
Tracking algorithm
Cloud height assignment algorithm
Result by new algorithm
Summary

## Slide 30
AMV derivation experiment using new tracking and HA technique
Satellite : MTSAT-2
Period : January 2013 (winter)
RTN
Target selection : MTSAT operational method
Tracking : Cross-Correlation
Height assign : operational method
TEST1
Target selection : MTSAT operational method
Tracking : Cross-Correlation, MLE using 5x5 and 15x15 pixels
Height assign : MLE height estimation using only radiance information
TEST2
Target selection : MTSAT operational method
Tracking : Cross-Correlation, MLE using 5x5 and 15x15 pixels
Height assign : MLE height estimation using radiance and tracked motion
Temporal information for tracking is not used in this experiment
for simplifying comparison using QI (consistent vector shows high quality even case that temporal QI is low)

## Slide 31
IR upper level AMV O-B statistic for January 2013
operation
TEST1 : radiance only
TEST2 : radiance and motion
QI>80
QI>80
QI>80
QI>80
QI>80
QI>80

## Slide 32
Full Disk
NH
TROP
SH
IR upper level AMV O-B statistic for January 2013
TEST1 : radiance only
TEST2 : radiance and motion
QI>80
QI>80
QI>80
0 m/s

## Slide 33
HIGH LEVEL |  |  |  |  |  |  |  |  |  | 
 | FULL DISK | NH | TROP | SH |  |  | FULL DISK | NH | TROP | SH
MVD | 4.81 | 7.22 | 4.45 | 5.48 |  | MVD | 5.88 | 6.34 | 5.77 | 5.91
RMSVD | 5.79 | 8.65 | 5.23 | 6.63 |  | RMSVD | 7.15 | 7.57 | 7.06 | 6.99
BIAS | -0.7 | 0.31 | -0.94 | 0.71 |  | BIAS | -1.34 | -1.20 | -1.53 | 0.31
SPD | 15.09 | 35.40 | 11.78 | 23.73 |  | SPD | 18.31 | 36.90 | 13.27 | 25.84
MEDIUM LEVEL |  |  |  |  |  |  |  |  |  | 
 | FULL DISK | NH | TROP | SH |  |  | FULL DISK | NH | TROP | SH
MVD | 6.17 | 6.57 | 3.93 | 5.28 |  | MVD | 5.28 | 5.50 | 3.76 | 5.27
RMSVD | 7.74 | 8.23 | 4.54 | 6.04 |  | RMSVD | 6.4 | 6.67 | 4.21 | 6.20
BIAS | -1.67 | -2.08 | 0.01 | -0.01 |  | BIAS | -0.69 | -0.85 | -0.17 | 0.29
SPD | 21.38 | 23.14 | 9.43 | 19.65 |  | SPD | 22.02 | 23.94 | 9.74 | 19.84
IR upper level AMV sonde statistics for January 2013
Method : Comparison of rawinsonde winds with AMV
winds within 150 km radius of a RAOB site
Filters : VERT. DIST.(>=700hPa) < 50 (hPa)
VERT. DIST.(<700hPa) < 35 (hPa)
QUALITY >= 85
0.5*0.5 deg. latitude/longitude grid point data
SPEED DIFF. < 30 (m/s) - DIRECTION DIFF. < 90 (deg)
RTN
TEST1
Only radiance information used

## Slide 34
HIGH LEVEL |  |  |  |  |  |  |  |  |  | 
 | FULL DISK | NH | TROP | SH |  |  | FULL DISK | NH | TROP | SH
MVD | 4.81 | 7.22 | 4.45 | 5.48 |  | MVD | 5.04 | 6.51 | 4.63 | 5.96
RMSVD | 5.79 | 8.65 | 5.23 | 6.63 |  | RMSVD | 6.03 | 7.79 | 5.45 | 6.98
BIAS | -0.7 | 0.31 | -0.94 | 0.71 |  | BIAS | -0.34 | -1.04 | -0.21 | 0.04
SPD | 15.09 | 35.40 | 11.78 | 23.73 |  | SPD | 19.26 | 37.21 | 14.42 | 27.57
MEDIUM LEVEL |  |  |  |  |  |  |  |  |  | 
 | FULL DISK | NH | TROP | SH |  |  | FULL DISK | NH | TROP | SH
MVD | 6.17 | 6.57 | 3.93 | 5.28 |  | MVD | 5.06 | 5.29 | 3.89 | 6.14
RMSVD | 7.74 | 8.23 | 4.54 | 6.04 |  | RMSVD | 6.05 | 6.30 | 4.53 | 7.13
BIAS | -1.67 | -2.08 | 0.01 | -0.01 |  | BIAS | 0.85 | 1.06 | -0.59 | 2.88
SPD | 21.38 | 23.14 | 9.43 | 19.65 |  | SPD | 21.16 | 23.82 | 10.11 | 25.78
IR upper level AMV sonde statistics for January 2013
Method : Comparison of rawinsonde winds with AMV
winds within 150 km radius of a RAOB site
Filters : VERT. DIST.(>=700hPa) < 50 (hPa)
VERT. DIST.(<700hPa) < 35 (hPa)
QUALITY >= 85
0.5*0.5 deg. latitude/longitude grid point data
SPEED DIFF. < 30 (m/s) - DIRECTION DIFF. < 90 (deg)
RTN
TEST2
Both of radiance and motion vector information used

## Slide 35
IR lower level AMV O-B statistic for January 2013
operation
TEST1 : radiance only
TEST2 : radiance and motion
QI>80
QI>80
QI>80
QI>80
QI>80
QI>80

## Slide 36
WV cloudy AMV O-B statistic for January 2013
operation
TEST1 : radiance only
TEST2 : radiance and motion
QI>80
QI>80
QI>80
QI>80
QI>80
QI>80

## Slide 37: Summary
By deriving motion vectors from sum of four correlation surfaces derived from small, large target boxes, and from forward and backward matching, Tracking accuracy was improved.
BIAS and RMSVD of MTSAT IR AMV are totally improved by proposal height assignment method in case to use only radiance information. But as for BIAS, quality debased over tropical region.
As a result to use motion vector as auxiliary information for height assignment, error and its homogeneity are improved, but positive BIAS can be seen in southern hemisphere.